## Slide 1: General Safe Driving Practices for Snowplow Operators Created for Clear Roads by the Virginia Tech Transportation Institute
Notes: Photo: Clear Roads
NARRATION: Welcome to Clear Roads’ General Safe Driving Practices for Snowplow Operators. This training course will cover information you can use to prevent incidents where you, as the snowplow operator, run into something. Common examples of these include fixed object strikes, run-off-road crashes, and backing crashes.

## Slide 2: Training Overview
Introduction
Strategies you can use to prevent crashes
  Hazard identification
  Proper backing
  Limiting distractions
  Fatigue management
Summary
Notes: Photo: Clear Roads
NARRATION: “Here is an overview of this safe driving training module for snowplow operators. Strategies to be discussed in this training include hazard identification, proper backing procedures, limiting distractions while driving, and fatigue management. This will be followed by a summary of these strategies. The presentation includes short video clips that demonstrate the strategies and periodic quizzes to gauge learning.”

## Slide 3: Training Objectives
Know common fixed object hazards
Visual scanning practices to identify fixed object hazards
Understand tips to identify and respond to hidden hazards
Describe strategies to prevent fixed object strikes
Define G.O.A.L.
Describe safe backing procedures
Identify alternatives to backing
Notes: NARRATION: “After completing this course, you will be to: understand the common fixed object hazards snowplow operators face, identify visual scanning practices that will be helpful in identifying fixed object hazards, understand tips to identify and respond to hidden hazards, describe strategies to prevent fixed object strikes, define G.O.A.L., describe safe backing procedures, and identify alternatives to backing.”

## Slide 4: Training Objectives, Continued
Define distracted driving
Identify types of distraction
Describe tips to avoid distracted driving
Define fatigue
Understand factors that cause driver fatigue
Identify signs of fatigue
Self-assess fatigue levels
Identify fatigue countermeasures
Notes: Narration: ”Additionally, you will be able to define distracted driving, identify types of distraction related to driving, describe tips to avoid distracted driving, define fatigue, understand factors that cause driver fatigue, identify signs of fatigue, self-assess your level of fatigue, and identify fatigue countermeasures.”

## Slide 5: Thank you for your hard work
As a winter maintenance professional, your job is critical to the economy and safety of the general public.
You help keep all road users safe!
Notes: Photo: Virginia DOT
NARRATION: “As you know, your job is critical to ensuring the safety of the general public and to keeping the economy going during winter weather. We know this is not easy! Thank you for everything you do to keep us safe.”
Presenters may replace the photo on this slide with one of all your operators.

## Slide 6: Snowplow Crashes
The most common incidents with snowplow operators involve property damage
Often involve hitting a fixed object along the road or in a parking lot
  23.8% of reported crashes involved fixed object strikes
  8.5% of reported crashes involved backing crashes
  11.4% of reported crashes involved the snowplow operator running off the road
Fortunately, you can prevent these crashes!
Notes: Photo: Utah DOT
NARRATION: “As snowplow operators typically drive in dangerous conditions, crashes do occur. Fortunately, most of these crashes are relatively minor, such as fixed object strikes and backing crashes. These two types of crash account for over 30% of all snowplow-involved crashes. However, others can be much more costly and dangerous, such as run-off-road crashes, which account for over 11% of snowplow-involved crashes. Fortunately, there are things you can do to prevent them from occurring.”
AUDIENCE PARTICIPATION
The presenter should have a discussion with operators to gather their personal opinions and experiences with crashes or near crashes. Ask about what types of incidents occurred, what common factors lead to these incidents, and what were some of the things they may have done differently to help prevent it from occurring again in the future.

## Slide 7: Hazard Identification
Notes: Photo: Clear Roads
NARRATION: “Snowplow operators may be able to prevent some of these crashes with careful hazard identification strategies. Some of these strategies are covered in the defensive driving training; however, this lesson discusses the specific strategies related to fixed object collisions.”

## Slide 8: Objects to be aware of
Guard rails
Soft shoulders
Curbs
Mailboxes
Bridge abutments
Trees and their branches
Parked or stuck vehicles
Railroad tracks
Bridge joints
Potholes
Manholes and water valves
Roadway signs and posts
Notes: NARRATION: “All drivers need to pay careful attention to fixed objects, but you, as a snowplow operator, are at a higher risk of hitting a fixed object because you are required to drive closer to them to clear snow. Some of the fixed objects snowplow operators often hit are guard rails, soft shoulders, curbs, mailboxes, bridge abutments, trees and their branches, vehicles parked by the curb or on the side of the road, vehicles that are stuck in snow, railroad tracks, bridge joints, potholes, manholes and water valves of multiple utilities, roadside posts, and roadway signs.”

## Slide 9: Visual Scanning for Fixed Objects
Objects may be hard to see when covered with snow
Look for clues that an object may be hidden
Continuously scan your surrounds
Don’t fixate on any one object or area
Use SIPDE
Notes: Photos: VTTI
NARRATION: Although many of these fixed objects are easy to see when there is no snow, they often become covered during winter weather. This makes them difficult to see. It is important for you to look for clues that an object may be hidden under snow. In the top photo, there is a curb circled in red. As you can see, it is barely visible. However, there are clues there is a curb. For example, you can see the curb to the left of the red circle. In the bottom photo, you can see that the snowplow operator hit the curb with the front plow. The now exposed curb is circled in red. This operator ran overtop of the curb because the operator did not continuously scan the surroundings. When you continuously scan the surroundings, you are more likely to noticed fixed object hazards. This means you should not keep your eye fixed on any one object for an extended period. To help prevent these events from occurring, remember the acronym SIPDE. Scan your surroundings, identify objects or vehicles that may be a hazard, predict if those objects or hazards may become a threat, decide how you should respond, and execute your plan.”

## Slide 10: Stay Vigilant
Maintain your situational awareness
  Be aware of where you are on the road
  How is your plow tracking?
  Are there obstacles in the path of your wings or front plow?
  Stay inside the fog line if unsure where the road edge is
Stay alert!
Notes: Photo: VTTI
NARRATION: “As you drive, it is important for you to maintain your situational awareness. To do this, notice where you are on the road and where your plow is in relation to fixed objects. This means looking ahead to see if there are any objects in the path of the plows. In this photo, you see a tractor trailer stuck on the right side of the road. This operator adjusted his front plow and raised his wing before passing this truck. Another suggestion from other snowplow operators is to not go outside the fog line if you are unsure where the edge of the road is. By staying inside the fog line, you know that you are not about to run off the road and hit any roadside objects. It is better to not clear a small portion of the road where vehicles will not drive than to run off the road, crash your vehicle, and be injured or killed. Finally, stay alert! If you are alert, you will recognize hazards in plenty of time to respond.”

## Slide 11: Make sure you’re aware of your surroundings
Notes: FACILITATOR NOTES: The snowplow is conducting plow operations along the shoulder of a road in falling snow with poor visibility. The snowplow approaches a disabled car stuck on the shoulder of the road and must move into the lane to go around. Occasional traffic is in the oncoming lane and passing the snowplow moving in the same direction. As the snowplow moves into the lane to go around the vehicle stuck on the shoulder, the snowplow sideswipes a light vehicle that was attempting to pass.
Potential Crash Factors related to the snowplow operator: 1) Poor visual scanning did not allow the operator to identify the fixed object, in this case the disabled car, early, and 2) The snowplow operator may have become complacent and failed to check his/her mirrors before making a lane change
NARRATION: “Here is an example of an incident involving a fixed object, in this case a disabled vehicle on the shoulder. Notice how the snowplow operator is clearing the shoulder of the road and there is occasional traffic passing the snowplow and in the oncoming lane. Is there anything you could have done differently to prevent this crash? First, the operator did not recognize the fixed object early. This led to the operator needing to change lanes at the last minute. Even though the operator did not hit the fixed object, it contributed to this crash. Additionally, the snowplow operator fails to adequately check the mirrors for adjacent vehicles. Partial blame could possibly be placed on the light vehicle driver if he or she was lingering in the snowplow’s no-zone or did not heed the snowplow’s turn signal.”

## Slide 12: Check on Learning #1: Visual Scanning
Which of the following is not a strategy that will help you avoid striking a fixed object?
  Continuously scan your surroundings
  Fixating on a single object
  Look for clues that objects may be hidden
  Be attentive to where your plow is tracking
Notes: Presenter should quiz audience to gauge learning.

## Slide 13: Check on Learning #1: Visual Scanning
Which of the following strategies will not help you avoid striking a fixed object?
  Continuously scan your surroundings
  Fixating on a single object
  Look for clues that objects may be hidden
  Be attention to where your plow is tracking
Notes: CORRECT ANSWER: You should not fixate on a single object as you drive. Fixating on a single object does not allow you to notice other approaching obstacles. Additionally, people tend to unintentionally steer towards in their direction they are fixated. This is often the opposite direction they need to do.

## Slide 14: Predicting Hidden Objects
Get to know your route before winter weather arrives
Look for risky areas and objects as your drive
  Objects close to the road
  Low objects that may become covered with snow
  Areas that historically have issues
  Intersections
  Urban areas
  Areas with soft shoulders
Notes: Photo: VTTI
NARRATION: “In this photo, a hidden hazard is circled in red. This is a rock or raised earth that has been covered. In this case, the operator does not notice the hidden object and hits it. If this operator was familiar with the route, it is very likely this strike would have been avoided. This is because the best way to predict where hazards are hidden by fallen snow is to know your route like the back of your hand. This means driving your route multiple times prior to any winter weather. As you drive your route, pay attention to any objects close to the road that could be hit by the plow, other low objects that could easily be covered by snow, areas that have issues in previous storms, intersections, urban areas, and roadways with soft shoulders.”

## Slide 15: Mark Known Hazards
If safe, mark known hazards on the roadway with delineator posts
Notes: Photos: Clear Roads
NARRATION: “It is also a good idea to mark any known hazards with delineator posts (if the posts do not create an additional hazard). In the top right photo, the edge of this road has been marked with delineator post so that the snowplow operator and all other road users know where the shoulder is. In the bottom left photo, obstacles are marked with posts so that the snowplow operator can avoid them.”

## Slide 16: Document and Track Hazards
Document known hazards and locations
Add new hazards as you notice them throughout the season
Always review the hazards on your route before beginning your shift
  New hazards may be marked
Notes: This Photo by Unknown Author is licensed under CC BY-SA
NARRATION: “One great suggestion by winter maintenance agencies is to create a database of all known hazard locations. This database could be made using GIS. However, any type of database could be used. These databases allow operators to keep track of where potential hazards are located. Operators can review this database before every shift to remind them where trouble spots may be. To make the most of these databases, operators should add new hazards as soon as possible.”

## Slide 17: Check on Learning #2: Hidden Objects
Which of these strategies will help prevent fixed object strikes?
  Mark known objects with delineator posts
  Document known hazards and locations
  Get to know your route before a winter storm
  All the above
Notes: Presenter should quiz audience to gauge learning.

## Slide 18: Check on Learning #2: Hidden Objects
What is a strategy to help prevent fixed object strikes?
  Mark known objects with delineator posts
  Document known hazards and locations
  Get to know your route before a winter storm
  All the above
Notes: CORRECT ANSWER: All these strategies help prevent fixed object strikes.

## Slide 19: Responding to Fixed Object Hazards
Do not overcompensate
  Remain calm
  Slow acceleration or deceleration
  Smooth steering wheel movements
Remove foot from accelerator
Check mirrors
Adjust plow height and position
Notes: This Photo by Unknown Author is licensed under CC BY-SA
NARRATION: “If you notice that you are about to strike a fixed object, remain calm and don’t overreact. Overreacting often can cause you to lose control of your vehicle. Instead, slowly accelerate away from it or brake while smoothly steering. Try not to make rapid steering wheel movements. This can cause you to lose traction on snow or ice. Also remember to always check your mirrors before making a lane change because another vehicle may be beside you. Finally, many fixed object strikes can be avoided by simply adjusting your plow height and position before reaching the hazard.”

## Slide 20: Safe Operating Speeds
Drive according to conditions
Review your agencies’ policies on plowing speeds
Recommend maximum of 30 mph while plowing in most situations
Notes: This Photo by Unknown Author is licensed under CC BY-NC-ND
NARRATION: “Going too fast for conditions is a major cause of many crash types, including fixed object strikes. If you keep your speeds slow, you will have more time to respond to fixed objects. Many of snowplow managers recommended keeping plowing speeds below 30 mph. However, review your agencies’ recommendations and policies before plowing. Also, if visibility is limited, 30 mph may be too fast. Always adjust your speed based on the road and weather conditions.”
FACILITATOT NOTES: If your agency has a recommended plow speed, place it on this slide.

## Slide 21: Other strategies to Prevent Fixed Object Strikes
Be familiar with all your equipment before a storm
Proactively adjust the plow
Plow only on paved surfaces
Don’t push the edge line
Notes: Photo: Clear Roads
NARRATION: “There are other strategies you can use to help prevent fixed object collisions. First, become familiar with all your equipment before the storm, including where all the controls are. Second, be sure to proactively adjust your plow. Be sure to raise or angle the plow appropriately as you approach bridge joints, manholes, curbs, etc. Third, many snowplow managers recommended only plowing on paved surfaces. Once the plow hits a soft shoulder, it can pull the truck off the road. To do this, don’t push the edge line on the road. If you are unsure where the edge of the road is, don’t go outside the fog line.”

## Slide 22: Safe Backing
Notes: Photo: Clear Roads
NARRATION: “This section of training discusses strategies you can use to safely back.”

## Slide 23: Common Causes of Backing Crashes
Backing crashes are almost always preventable!
Causes
  Fatigue
  Impatient
  Distraction
  Poor Visibility
Notes: This Photo by Unknown Author is licensed under CC BY
NARRATION: “Backing crashes are some of the most frustrating types of crashes for many snowplow agencies. This is because nearly all of them are preventable. They are usually caused because you are tired from working a long shift, you are in a rush to complete a task, you are distracted by something inside or outside the vehicle, or you have limited visibility. Additionally, you may have equipment sticking out further behind you than you expect. Some of these pieces of equipment include: a spinner, a chute, trailer, lights, tanks, a raised box, or spray bar. If you aren’t careful, these pieces of equipment may strike something as you back up.“

## Slide 24: Common Backing Crash
Notes: Facilitator Notes: In this video, the snowplow operator pulls into the parking lot to turnaround. Have a discussion with your operators about why this crash occurred. Unfortunately, this is a common scenario even though it is 100% preventable. Some suggestions on how this could have been prevented include: pulling around the gap pumps to avoid backing, using a spotter, checking both mirrors while backing (the light pole cannot be seen in the right-side mirror but can be seen in the driver-side mirror), and getting out and looking prior to backing.
NARRATION: “Here is a common scenario. As you watch this video, think about how this crash could have been avoided? Unfortunately, this type of crash is very common with snowplows in parking lots and garages. Please be careful. It is always better to err on the side of caution, especially when unsure of the situation.”

## Slide 25: How could you have prevented that crash?
Why do you think that crash occurred?
What should you do different?
Notes: This Photo by Unknown Author is licensed under CC BY-SA
AUDIENCE PARTICIPATION
The presenter can discuss with the operators what they thought about the crash and discuss their thoughts on how it could have been avoided.

## Slide 26: Check on Learning #3: Backing
Nearly all backing crashes are preventable.
  True
  False
Notes: Presenter should quiz audience to gauge learning.

## Slide 27: Check on Learning #3: Backing
Nearly all backing crashes are preventable.
  True
  False
Notes: CORRECT ANSWER: This is true. Nearly all backing crashes are preventable.

## Slide 28: G.O.A.L. before Backing
G.O.A.L.
Get Out And Look!
Notes: NARRATION: “Before you back up, you need to G.O.A.L, Get Out And Look. This is especially true in parking lots as there are often many objects and obstacles you could hit.”

## Slide 29: Circle of Safety
When you G.O.A.L, don’t just look directly behind your vehicle
  Both sides
  Underneath
  Above
  Front
  Back
Examine the full path you intend to travel
Open garage doors and look
Notes: NARRATION: “When you G.O.A.L., you can’t just look directly behind your vehicle. You need to closely look at your entire circle of safety. This includes looking on both sides of the vehicle, underneath, above, in front, and in back. Additionally, it is important to remember to examine the entire area where you intend to back into. For example, if you are parked in the garage, remember to open the garage door and look outside. Don’t just look inside the garage door because there could be something on the other side you could hit. Finally, as you reach the top step of your vehicle before getting inside, take one more glance towards the rear of the truck. You want to do this just in case something or someone entered that space unknowingly at the last second.”

## Slide 30: Using Spotters
A second set of eyes will help you avoid obstacles while backing
If available, always have a partner get out and spot while backing
  Especially in tight spaces
If a spotter is not available, always get out and look
  Identify markers that can help you avoid objects
Notes: NARRATION: “In addition to walking around your vehicle before backing, spotters are an excellent way to ensure you don’t back into anything. If you have a partner in the vehicle with you or in the yard, ask them to be your spotter as you back up. This is especially important if you need to back into a tight space with many obstacles. If someone isn’t available to help, you must get out and look. Look for markers or other clues you can use to navigate tight spaces.”

## Slide 31: Recommended Signals
Notes: Photo: OSHA
AUDIENCE PARTICIPATION
The presenter can view these recommended signals to use with spotters. Include any other signals that may be common in your agency.

## Slide 32: Other Backing Suggestions
Warn others that you are about to back
Turn on the four-way flashers
Know your blind spots
Turn the radio(s) down
Stop all distractions
Slow!
Use all available mirrors
Notes: NARRATION: “There are a few more things you can do to be safe while backing in addition to G.O.A.L. and using spotters. First, you should always warn others that you are about to back up. Usually a simple honk of the horn is enough to let people know that you are about to back up. Second, some operators suggests turning on the four-way flasher while backing. Third, remember that you have limited visibility around the vehicle. Objects and people can disappear from your view. Fourth, turn down the radio volume. This will help you hear any other vehicles or indications that you need to stop. Fifth, don’t get distracted while backing up. Sixth, go slow. Seventh, make sure to use all your mirrors and continuously scan your surroundings.”

## Slide 33: Check on learning #4: Backing Countermeasures
Which of the following signals should a spotter use to indicate the remaining distance to an object?
Notes: Presenter should quiz audience to gauge learning.

## Slide 34: Check on learning #4: Backing Countermeasures
Which of the following signals should a spotter use to indicate the remaining distance to an object?
Notes: CORRECT ANSWER: The first signal lets a driver know the distance they have remaining before an object.

## Slide 35: Clearing turnarounds
Clear enough space so that you can turn without backing
Watch out for slopes
Careful of hidden objects
Notes: NARRATION: “Parking lots and yards are not the only space you need to be careful in while backing. Turnarounds are another location where many snowplows have crashes while backing up. To help reduce the risk of a backing crash at a turnaround, always try to clear enough space so that you turn without the need for backing or a 3-point turn. However, as you clear the turnaround, watch out for steep slopes or other areas where you could lose control or traction. Also, be on the lookout for hidden objects that may be covered with snow. Finally, unpaved turnaround locations may become soft if the ground is not frozen. Be careful so that you do not get stuck or slide down a slope due to soft ground.”

## Slide 36: Backing Alternatives
Pull through
Park on curb that does not require backing
Park away from other equipment or vehicles if backing out is required
Back into spaces upon arrival
Notes: NARRATION: “The most effective way to prevent backing crashes is to avoid backing-up whenever possible. This could mean you pull through spaces when possible or parking at the curb. However, there are times when you have to back-up. In these cases, the safest choice is to back into spaces when you arrive. Doing this gives allows you to see potential hazards better and reduces the risk that you will hit something. Additionally, if possible, you should try to park away from other equipment or vehicles if you must back-up. This just gives you more space to complete the maneuver safely.”

## Slide 37
Limiting Distractions
Notes: Photo: Clear Roads
NARRATION: “This section reviews the dangers of distraction and how you can limit them”

## Slide 38: What is Distracted Driving?
Notes: This Photo by Unknown Author is licensed under CC BY-SA-NC.
This Photo by Unknown Author is licensed under CC BY-NC-ND.
This Photo by Unknown Author is licensed under CC BY-SA.
This Photo by Unknown Author is licensed under CC BY-NC-ND.
NARRATION: “Distracted driving is doing anything that take your attention away from the driving task. Distractions include things that take your eyes away from the road, require you to remove your hands from the steering wheel, noises that take your attention away from driving, or intense emotions or thoughts that don’t allow you to fully focus on driving.”

## Slide 39: Distracted Driving Example
Notes: Video: US Department of Transportation, https://www.fmcsa.dot.gov/safety/driver-safety/cmv-driving-tips-driver-distraction
NARRATION: “Watch this video closely. The driver is clearly distracted by his cell phone. Try to see how long he has his eyes off the road. This driver was very lucky to avoid a head-on crash. If he would have kept his eyes off the road for one more second, he likely would been involved in a serious crash.”

## Slide 40: Danger of Distracted Driving
Multi-tasking involves switching your attention between two tasks
  You can not focus on two tasks at once, you switch back and forth
Especially dangerous when you are visually or manually distracted
  You can’t see if something unexpected happens in front of you!
23x more likely to the being involved in crash or near crash when texting
Notes: This Photo by Unknown Author is licensed under CC BY-NC-ND
NARRATION: “Distracted driving is dangerous because you can not focus on two tasks at once. Instead, you switch your attention between two or more tasks. This means that your attention may not be on what is happening around you. This is especially true if the distraction includes things that take your eyes off the road and your hands off the wheel. If your eyes are not looking forward, you will not notice if something unexpected happens in front of you. Research shows that when you do a visual-manual task while driving, such as texting, you are 23 times more likely to be involved in a near-crash or crash compared to when you are not texting.”

## Slide 41: Cognitive Distraction
“Daydreaming”
Distracted by our thoughts or emotions
Factors that often cause cognitive distraction
  During or after arguments
  Under pressure
  Family concerns
  In monotonous conditions
  Fatigued
Notes: This Photo by Unknown Author is licensed under CC BY-SA
NARRATIVE: “Most drivers have experienced cognitive distraction at least one time in their life. Have you ever suddenly realized that you can’t remember the last 5 minutes of a drive or that you missed your exit? These are examples of cognitive distraction. You can think of cognitive distraction as daydreaming or when your focus is not fully on driving because of your thoughts or emotions. There are many causes of cognitive distraction, but some of the most common causes of cognitive distraction are intense emotions like those felt during or after an argument, being under pressure at work or at home, being concerned about the wellbeing of friends or family, while driving on long drives or during monotonous conditions, and when you are fatigued. Do your best to avoid becoming distracted by these thoughts or emotions and always focus on the driving task.”

## Slide 42: Driver Tips to Avoid Inattention
Pay attention to what is happening in front of you
Keep your eyes on the road and your hands on the wheel
  Continue to scan for hazards
Know where you are going before you leave
Know what the traffic is doing around you
Watch out for other distracted drivers
Prevent “drift” lane departures
Notes: Photo: VTTI
NARRATION: “To avoid the risks of inattention, use the following tips: maintain your attention to what is happening in front of you on the roadway, keep your eyes on the road and your hands on the wheel, always scan for hazards, know your route before you leave, only engage in tasks related to plowing or driving, know what traffic is around you, watch out for other distracted drivers, and avoid unintentional “drift” lane departures.”

## Slide 43: Check on learning #5: Inattention
Which of the following is considered a driver distraction?
  Day dreaming
  Looking at cell phone
  Eating
  All the above
Notes: Presenter should quiz audience to gauge learning.

## Slide 44: Check on learning #5: Inattention
Which of the following is considered a driver distraction?
  Day dreaming
  Talking on a cell phone
  Eating
  All the above
Notes: CORRECT ANSWER: All these are considered distracted driving.

## Slide 45: External Distraction
  Being distracted by something outside of your vehicle
  8% of heavy vehicle crashes occurred due to driver external distraction.
  Examples
    Unfamiliar with road
    Searching for an address
    Construction activity
    Looking at a building or scenery
    Looking at a sign
Notes: This Photo by Unknown Author is licensed under CC BY-SA
NARRATION: “Distractions are not only inside the cab of the vehicle. They can also be external. These types of distractions cause 8% of heavy vehicle crashes. Examples of external distraction include being unfamiliar with the road or a route, searching for an address, construction activity, looking at a building or scenery, and looking at a sign.”

## Slide 46: External Distraction
Notes: Video: US Department of Transportation, https://www.fmcsa.dot.gov/safety/driver-safety/cmv-driving-tips-driver-distraction
NARRATION: “Here is a video of a driver experiencing a near-crash due to an external distraction. About half through the video, the driver gets distracted by something on the right side of the road. Traffic slows ahead of the driver at the same time. The driver fortunately looked ahead in time and was able to respond; however, it was a close call.”

## Slide 47: Tips to Avoid External Distractions
Give the drive your full attention
Keep your eyes on the road, scanning for hazards
Avoid fixating on people, animals, objects, or events not related to driving
Stop and seek advice on an alternative road if you are diverted from your planned route
Notes: Photo: VTTI
NARRATION: “To avoid external distractions, avoiding staring at an outside person, animal, object, or event not related to driving for an extended period. Instead, give the drive your full attention and don’t take your eyes off the road for an extended amount of time. If you get lost or if the road is blocked, stop and seek advice from dispatch on an alternative route.”

## Slide 48: Internal Distractions
  Being distracted by something inside your vehicle
  2% of heavy vehicle crashes occurred due to driver internal distraction.
  Usually initiated by the driver
    Texting/App use
    Dialing a phone
    Looking at GPS screen
    Retrieving objects
    Reading
Notes: This Photo by Unknown Author is licensed under CC BY-ND
NARRATION: “The most dangerous distractions usually are inside the vehicle. Internal distractions cause about 2% of heavy vehicle crashes. These are usually the most dangerous because they take your eyes of the road for the longest amount of time. Some examples of internal distractions are texting/phone applications, dialing a phone, looking at a GPS screen, reaching for an object inside the vehicle, and reading.”

## Slide 49: Tips to Avoid Internal Distractions
Limit internal distractions to necessary job duties
Properly adjust your seat and mirrors before driving
Clean the vehicle of any unnecessary personal belongings
Avoid smoking and/or lighting a cigarette while driving
Limit amount of time for legal phone use
  No texting, manual dialing, surfing internet, app use, chat programs, etc.
    Only safe time is when you are off the road and in park
    It is still risky if you are stopped at an intersection, stop light, etc.
Notes: NARRATION: “Always limit what you do while driving to those things necessary for your job. To avoid becoming distracted by an internal object, you should properly adjust your seat and mirrors before driving. This allows you to safely see out your mirrors and easily reach the controls. If you adjust these while driving, you will often be forced to take your eyes off the road. Do not try to look for an object in the cab while you are driving. Instead stop the vehicle before searching. Also, make sure the vehicle is clear of any unnecessary objects. These objects could move around in the vehicle while driving and cause a distraction. Also, avoid smoking or lighting a cigarette while driving. These tasks often require taking your eyes off the road and your hands off the wheel. Additionally, falling embers and ash often creates an unsafe hazard inside the vehicle. Finally, limit the amount of time you legally use a phone. Do not text, manually dial the phone, surf the internet, use applications, chat programs, etc. while driving. The only safe time to perform these phone features is when you are off the road and not moving. ”

## Slide 50: More Tips for Internal Distractions
Do not attempt to read or write while you drive
Avoid eating and drinking while you drive
Review maps and plan your route before getting behind the wheel
Limit conversations with others to job related subjects, including radio conversations
Notes: Photo: VTTI
NARRATION: “Other tips to avoid internal distractions include do not attempt to read or write while you drive, avoid extended periods of eating and drinking while you drive, review any maps and plan your route before starting your drive, and limit conversations with others to job related subjects, including conversations over the radio.”

## Slide 51: Check on Learning #6: Internal and External Distractions
How can you avoid internal distractions while driving?
  Keep your phone handy in case someone calls you
  Avoid looking at your cell phone
  Allow the cab of the truck to be cluttered
  Review maps while driving
Notes: Presenter should quiz audience to gauge learning.

## Slide 52: Check on Learning #6: Internal and External Distractions
How can you avoid internal distractions while driving?
  Keep your phone handy in case someone calls you
  Avoid looking at your cell phone
  Allow the cab of the truck to be cluttered
  Review maps while driving
Notes: CORRECT ANSWER: You should avoid being cogitative distracted while driving. This include avoiding complex or emotionally intense conversations.

## Slide 53
Fatigue Management
Notes: Photo: Clear Roads
NARRATION: “This section describes proper fatigue management.”

## Slide 54: What is Fatigue?
Reduced alertness
Reduced attention to the environment
Decrease in performance
Increased irritability
Poor judgement
Sleepiness
Notes: Photo: North American Fatigue Management Program
NARRATION: “Fatigue and sleepiness are often used interchangeably. Although there are some differences, for the purposes of this training we are going to consider them to be the same. This lesson discussing drivign fatigue, which is different than muscle fatigue. Being physically tired from activity usually does not result in poor driving. However, driving fatigue does. Driving fatigue usually includes reduced alertness, reduced attention to what's going on around you, decreased driving performance, increased irritability, poor judgement, and an increase in sleepiness.”

## Slide 55: Fatigue Example
Notes: Video: US Department of Transportation, VTTI
NARRATION: “Here is an example of what fatigue looks like. In the top left you can see the driver’s face. In the top right you can see out the front windshield. In the bottom left you can see the view in the left-side mirror on the side of the truck. In the bottom right, you can see the view in the right-side mirror on the side of the truck. Watch the driver’s face. He is clearly getting tired. The driver is having difficulty keeping his truck in a straight line, and eventually drifts towards the end of the right shoulder and almost hits the guard rail.”

## Slide 56: How common is snowplow operator fatigue?
Majority of snowplow operators report feeling fatigued during a shift
  75% to 80% of snowplow operators feel fatigue sometimes while driving
  12% to 15% of snowplow operators feel fatigue most of the time or always while driving
28% of snowplow operators have shifts longer than 12 hours
  Reports of fatigue significantly increase with shifts 16+ hours long
Notes: NARRATION: “Driver fatigue is dangerous because it significantly increases your risk of a crash. This is especially important for snowplow operators because fatigue is common in your occupation. Over 75% of snowplow operators report feeling fatigued sometimes while operating a snowplow. A further 12% to 15% report feeling fatigued almost all the time or always while operating a snowplow. One of the reasons fatigue is so common with snowplow operators is due to long shift lengths. 28% of snowplow operators reported shifts longer than 12 hours. Reports of fatigue significantly increase with shifts longer than 16 hours, however, all shifts longer than 12 hours also are associated with increased reports of fatigue.”

## Slide 57: Common causes of driver fatigue
Sleep-Related Causes of Fatigue
Prior sleep quantity and quality
Time of day
Time since last sleep
Health
Task-Related Causes of Fatigue
Monotonous driving conditions
Complex tasks
Time-on-task
Equipment
Notes: NARRATION: “There are two types of fatigue: sleep-related fatigue and task-related fatigue. Sleep-related causes of fatigue include getting a bad night of sleep, less sleep than normal, being awake during the hours between 12:00am and 6:00am, the amount of time that has passed since you last slept, and your health. Task-related causes of fatigue include monotonous driving conditions, poor visibility, complex driving tasks, extend periods of time-on-task, and excessive vibrations and noise from equipment.”

## Slide 58: Check on learning #7: causes of fatigue
What is not a cause of sleep-related fatigue?
  Time of the day
  Poor sleep
  A long, boring drive
  Poor health
Notes: Presenter should quiz audience to gauge learning.

## Slide 59: Check on learning #7: causes of fatigue
What is not a cause of sleep-related fatigue?
  Time of the day
  Poor sleep
  A long, boring drive
  Poor health
Notes: CORRECT ANSWER: A long, boring drive is a task-related cause of fatigue.

## Slide 60: Signs of Fatigue
Attention to detail decreases
Daydreaming
Slow responses and reaction time
Reduced motivation
Poor memory
Tunnel vision
Microsleeps
Notes: Photo: North American Fatigue Management Program
NARRATION: “The good news for you is that there are signs of fatigue you can identify. These include your attention to detail decreases, you start to daydream more, you have slowed responses and reaction time, your motivation decreases, you have poor memory, you experience “tunnel vision”, and you have microsleeps. Microsleeps are when you “nod off” unintentionally for brief periods of time.

## Slide 61: Assessing your Own Fatigue
Rubbing the face or eyes
Yawning
Nodding head
Scratching
Moving restlessly in the seat
Tunnel vision
Drifting between lanes, tailgating, or missing traffic signs
Jerking the truck back into the lane
Drifting off the road and narrowly missing a crash
Notes: Photo: VTTI
NARRATION: “As you drive, it is important for you to assess your own level of fatigue. To self-assess if you are fatigued, notice if you are rubbing your face or eyes, are excessively yawning, nodding off, scratching, moving restlessly in your seat, have tunnel vision, drifting between lanes, tailgating, missing traffic signs, jerking the truck back into the lane, and/or drifting off the road or onto the shoulder unintentionally. These are all signs that you are becoming fatigued and should take a break from driving.”

## Slide 62: Driver Tips to Reduce the Risk of Fatigue
Recognize the signals and dangers of drowsiness
Do not upset your body clock more than necessary
Avoid any kind of medication or drugs that induce drowsiness or have warning labels against operating vehicles or machinery
Do not only rely on coffee, radio, open window, or other tricks to keep you awake
Ensure you obtained adequate sleep prior to your shift
Notes: NARRATION: “There are things you can do to help prevent fatigue from developing. First, make sure you get enough sleep before your shift. Experts say 7 to 8 hours of sleep is needed to feel fully rested. Do your best to get this amount of sleep before coming to work. Second, recognize the signals and dangers of drowsiness. Know how to self-assess fatigue while you drive. Third, do your best to maintain a sleep schedule. We tend to get sleepy at the same times every day, so try to maintain the same schedule as much as possible. Of course, this is not always possible during winter emergencies, so recognize that you are more suspectable to fatigue during the hours that you are normally asleep. Fourth, avoid taking any kind of medications that may cause drowsiness. Review your medications and look for warning labels that indicate against operating heavy machinery. Finally, do not simply rely on coffee, the radio, and open windows, or any other tricks to keep you awake. Some of these tricks may help, but their effects are short lived. For example, listening to the radio does help reduce fatigue, but only for a short amount of time.”

## Slide 63: Breaks from Driving
Breaks give your mind a rest and can help reduce fatigue
Take breaks from driving whenever you can
  At least every 2 hours
  Get out at each turnaround
  When refilling material
Walk around your truck and stretch
Notes: NARRATION: “If you do notice that you are fatigued, one of the best ways to reduce fatigue is to take a brief break from driving. Breaks give your mind a rest from the driving task. When plowing, it is recommended to take a break whenever you can, but at least once every 2 hours. However, more frequent breaks are better. For example, at each turnaround, get out of the truck briefly and walk around and stretch. Also, anytime you return to the yard to refill material, take a minute to get out of the truck.”

## Slide 64: Other Countermeasures of fatigue
Caffeine
Music can help for brief periods of time
  Can’t be the only countermeasure used
Improved cab insulation to reduce noise
Properly adjusted seat
Stay hydrated
Eat healthy
SLEEP!
Notes: Photo: North American Fatigue Management Program
NARRATION: “There are other things you can do to prevent fatigue. These include drinking caffeine, listening to the radio, improved cab insulation to reduce noise, a properly adjusted seat, staying hydrated, and eating healthy. However, do not rely on these countermeasures alone. The only remedy to fatigue is to get sleep!”

## Slide 65: Check on Learning #8: Combating Fatigue
Rolling down your window and playing the radio is the best way to reduce fatigue
  True
  False
Notes: Presenter should quiz audience to gauge learning.

## Slide 66: Check on Learning #8: Combating Fatigue
Rolling down your window and playing the radio is the best way to reduce fatigue
  True
  False
Notes: CORRECT ANSWER: The best way to reduce fatigue is sleep!

## Slide 67: Additional Resources
Clear Roads snowplow operator and manager training resources: https://clearroads.org/training-resources/
North American Fatigue Management Program: https://www.nafmp.com/
Network of Employers for Traffic Safety: https://driventowellness.org/
National Safety Council: https://www.nsc.org/work-safety/safety-topics/fatigue
Federal Motor Carrier Safety Administration’s Driving Tips: https://cms8.fmcsa.dot.gov/safety/driver-safety/cmv-driving-tips-overview

## Slide 68: Acknowledgements
This training was developed by the Virginia Tech Transportation Institute, Center for Truck and Bus Safety
  Matt Camden: mcamden@vtti.vt.edu
  Jeff Hickman: jhickman@vtti.vt.edu
  Rebecca Hammond: rhammond@vtti.vt.edu
  Scott Tidwell: stidwell@vtti.vt.edu
  Richard Hanowski: rhanowski@vtti.vt.edu
Clear Roads Technical Advisory Committee
  Doug McBroom, Clay Adams, James Stevenson, Brian Burne, Steve Spoor, Larry Gangl, Tom Peters, Mark Trennephl
Example existing training provided by the Colorado DOT, Montana DOT, and the Virginia DOT

## Slide 69: Clear Roads
This presentation was developed with funding from the Clear Roads research program, which brings together transportation professionals and researchers from around the country to drive innovation in the field of winter maintenance.
Find additional information and resources at
http://clearroads.org/
Notes: Photo: Clear Roads

## Slide 70: Thank you for your dedication, Plow Safely!
Notes: Photo: Clear Roads